Documentation for the program "fourfit"
-- last update 2012.3.21
---------------------------------------

COMMAND NAME:   fourfit

SYNOPSIS:  Performs fringe searching for continuum MkIV data

SYNTAX:  fourfit [-a] [-b BB:F] [-c controlfile] [-d display device]
            [-f value] [-m value] [-n value] [-p] [-r afile] [-s naps]
            [-tux] [-P polar_pair] [-T trefoffs] [-X] data file list 
            [set <control file syntax statements>]
         Where all arguments except the data file list are optional.
         The [-r afile] option replaces the data file list, however.
         The "set" argument and the commands which follow it must
         come last.  All option flags must appear before the data file
         list.  Option flags can come in any order.

    Here are two examples of command-line invocations of fourfit, with
    an explanation of what they do:

fourfit -txas -m 1 -c control 018-234505 set mb_win -0.0034 .004 freqs a b
        Test mode, xwindow display, accounting switched on, cross
        power spectrum plot switched on, moderately verbose, use
        control file named "control" in current working directory,
        process all data in scan directory 018-234505, override
        multiband delay search window and select channels 'a' and
        'b' only.

fourfit -r refr_list -c control -d hardcopy -b AT:S
        Process all data referenced by type 2 lines in the A-file
        named "refr_list", use control file "control", print the
        fringe plot on the default printer, process only baseline
        AT frequency subgroup S.

OPTION FLAGS:
        -a
            If specified, this option switches on accounting
            of CPU time and wall-clock time used in the various
            parts of fourfit.  When the program finishes, it
            produces a summary of these timing statistics.

        -b BB:F
            Allows the user to override the control file
            with a specification of the baseline and/or
            frequency group to be processed.  The syntax is
            flexible.  0, 1 or 2 characters before the colon
            refer to the baseline (one character is interpreted
            as a station), and 0 or 1 character after the colon
            is interpreted as the frequency subgroup.  You can
            use the control file wildcard character '?' in
            the baseline, but remember to protect it from the
            C-shell either by escaping it with a backslash '\'
            or enclosing the entire -b argument in single
            quotes.  If you wish only to specify the baseline,
            the colon may be omitted.  An error in the -b
            flag argument causes the flag to be ignored, and
            fourfit will continue execution.

        -c controlfile
            Specifies the file which contains parameters
            to control the operation of the program.  If
            absent, fourfit will use only the file pointed to
            by the environment variable DEF_CONTROL, which
            in turn defaults to $FF/cf_default as defined
            in the $HOPS/setup.csh file.  Any parameters
            set in a control file specified with the -c option
            override the default file values.  A description
            of the syntax of the control file, with an example,
            can be found later in this document.

        -d display_device
            Upon completion of a fringe fit, fourfit can
            optionally display the results using postscript.
            The valid choices for "display_device" are:
                diskfile:file.ps  save the plot in "file.ps"
                hardcopy          send the plot directly to lpr
                pshardcopy        print the plot via pplot_print
                xwindow           show the plot in an X11 window
                psscreen          the same, but allow GS_* options

        -f first channel
            overrides the default first channel (0) to facilitate
            plotting when there are more than 16 channels (see -n)

        -m value
            This flag controls the verbosity of the program via
            the integer argument "value", which ranges from 3
            (virtually silent except for major errors) to -3 
            (incredibly verbose, of use only to the authors of 
            the program).  The default is 2.

        -n number of channels
            When channels are overridden (see also the -f flag)
            this tells how many channels to put on the plot. Note
            that neither -f nor -n affect the actual fringe fit,
            just the plotting thereof.

        -p 
            This is equivalent to "-d psscreen".

        -r afile
            Puts fourfit into "refringe" mode.  Fourfit refringing
            is driven by an A-file input, which overrides any 
            correlator root files directly specified on the command
            line (i.e. the latter are ignored when the -r flag
            is specified).  The input A-file, of which there can
            be only one, may contain root, corel or fringe lines,
            but only the fringe lines are used to determine which
            data to process, by baseline and frequency subgroup.
            Obviously, the -r flag is inconsistent with the -u
            flag, and specifying both is an error.  Note that for
            afiles using HP-1000 (version 1) line formats, fourfit
            has to pre-check the disk for the existence of the 
            type 2 files.  The data area is controlled by the
            DATADIR environment variable.  It defaults to the
            value of $CORDATA.

        -s naps
            This parameter controls how many AP's are merged
            together into each plotting segment. Thus the number
            of time points shown in the phase, amplitude, and
            validity plots is so controlled. Additionally, the
            ph/seg and amp/seg statistics are calculated based
            upon the stated number of AP's in each segment.

        -t
            This flag places fourfit in test mode.  Everything
            works as normal, except that the output file is not
            written to disk, and the root file is not updated.
            This is useful when experimenting with different
            fringe-fitting strategies, in order to avoid cluttering
            up the disk.

        -u
            Normally, fourfit processes all data consistent with
            the data file list and the control information.  When
            this flag is specified, fourfit will also check the
            information in the type-2100 record of the root to 
            see if the data have already been processed by fourfit.
            If so, the data in question are skipped.  The "u"
            stands for update mode.

        -x
            This is equivalent to "-d xwindow".

        -P pp
            Controls polarization processing, where the 2 character
            string pp is one of four cross-polarization 
            states {RR, LL, RL, or LR}

        -T trefoffs
            If this option is invoked, the fourfit reference
            time will be calculated by taking the nominal scan
            start time from the ovex file and adding trefoffs
            (which is an integer # of seconds) to it.

        -X
            Forces fourfit to write cross-power spectra into
            type 230 records. This option is typically used for
            import into AIPS.

ARGUMENTS:  data file list
            This mandatory argument or arguments tells fourfit
            which data files to process.  The format of the data
            file specification is the standard one for all MkIV
            software.  You may specify individual filenames, 
            scan directories which contain data files, 
            experiment directories, or any combination of
            these three.  In the latter two cases,
            fourfit will descend the directory tree looking for
            data files to add to its internal list of files to
            process.  Only root files need be specified.  The
            data files actually fringe-searched are determined
            by the combination of the root files specified and the
            restrictions imposed by the control file or control
            parameter list (see below).  In the absence of 
            such restrictions, all data associated with the 
            specified root files are processed.

            Beware of trying to specify too many files or scan
            directories, as it is possible to overflow the Unix
            argument list buffer on large experiments.  In such
            cases, specify the experiment directory instead.

	    The postscript rendering is performed by ghostscript
	    [gs(1)], and GS_* environment variables can be used
	    to produce a variety of graphics when the "psscreen"
	    (see -d above).  For example,

		GS_OPTIONS=-sOutputFile=abc.png GS_DEVICE=png16 \
		fourfit ...

	    will generate a 16-color PNG plot.

        set <control file syntax statements>
            This command line argument is optional, and
            is intended to permit rapid, temporary modification
            of 'fourfit' behaviour without the need to edit the
            control file.  The word "set" tells fourfit to expect
            additional control information on the rest of the
            command line.  The syntax of this control information
            is identical to that of the control file (see
            detailed description below).  The control file
            parser will detect syntax errors and abort if you
            do not follow the rules as laid down.  The control
            information you specify after the "set" argument
            on the command line applies to all data to be
            processed, and overrides whatever the control file
            itself specified for the parameters in question.

ENVIRONMENT:    DEF_CONTROL, DISPLAY, DATADIR, GS_DEVICE, GS_OPTIONS

DESCRIPTION:

Fourfit is the functional analogue of FRNGE on the HP-1000 systems, and
searches the data represented by the root and corel files for fringes,
writing the results of the search to files of type fringe.  The emphasis
in the design of the program has been speed and flexibility, particularly
with regard to future enhancements.  Algorithmically, the program is
closely modelled on FRNGE, with only minor enhancements as yet, based on
the availablity of greater computing resources.

Below is a preliminary form of a document describing in detail the format and
syntax of the control file:

* Example of current syntax for fourfit control file
* This file makes no semantic sense for a real experiment; rather, it is used
* to illustrate typical command syntaxes.

max_parity 0.001                       * global commands come first
ref_freq  8213.15 
x_crc       discard 
x_slip_sync keep  
y_slip_sync discard
start -10
use_samples true

if station L and f_group X
   freqs a+ b c d- e f g h
   pc_phases abcdefgh 5 -11 12 38 -56 13.2 11 -29
   pc_mode ap_by_ap
   pc_freqs abcdefgh 10 10 1010 10 1010 10 1010 1010

if station L and f_group S
   pc_phases ijkmn 4.5 -78 39 +12 0
   pc_mode normal

if station A
   pc_mode multitone
   pc_period 30
   pc_tonemask abcdefgh 0 0 8 0 4 0 5 0
   pc_phases_l abcdefgh 12 13 11 12 24 -6 38 110
   pc_phases_r abcdefgh 11 29 14 11 64 -2 44 132
   samplers 2 abcd efgh
   pc_delay_l 30.2
   pc_delay_r -5.9
   ionosphere 18.0

if (station V or baseline KT) and source 3C279       * parentheses NYI
   sb_win -0.5 0.5    mb_win 0.02 0.02  dr_win -1.0E-6 0.5E-6

else
   sb_win 0.0 0.0     mb_win 0.02 0.02  dr_win -1.0E-6 0.5E-6

if scan 288-210210
   sb_win .37 .37

if scan > 289-132510
   skip true

if baseline K? and not scan 250-120000 to 251-235959
   switched scan_start
   period 30
   gates abcfgh  0 30  0 10  15 25     0 10  15 25  0 30


* End of sample control file



SELECTOR KEYWORDS       VALUES
   station            1 character
   baseline           2 characters
   source             string of 1-8 chars
   f_group            1 character
   scan               UT-epoch (special format), or:
              < UT-epoch
              > UT-epoch
              UT-epoch1 to UT-epoch2  (inclusive time range)



SYNTACTIC KEYWORDS
   if
   else   (NYI)
   and
   or
   not
   ()     (NYI)
   <>
   to
   ?

ACTION KEYWORDS         VALUES
   adhoc_amp          float
   adhoc_period       float
   adhoc_phase        'sinewave' or 'polynomial'
   adhoc_poly         <7 floats/integers (mixture OK)
   adhoc_tref         float
   dc_block           `true' or `false' (default: false)
   dec_offset         float
   delay_offs         n char string, followed by n floats
   dr_win             2 floats
   fmatch_bw_pct      float
   freqs              n chars
   gates              n char string, followed by 2n floats
   index              n ints
   interpolator       'iterate' or 'simul' (default: iterate)
   ionosphere         float
   ion_npts           int
   ion_win            2 floats
   lsb_offset         float
   max_parity         float
   mb_win             2 floats
   optimize_closure   'true' or 'false' (default: false)
   passband           2 floats
   period             int
   pc_amp_hcode       float
   pc_delay_l         float
   pc_delay_r         float
   pc_phases          n char string, followed by n floats
   pc_phases_l        n char string, followed by n floats
   pc_phases_r        n char string, followed by n floats
   pc_freqs           n char string, followed by n floats
   pc_mode            `normal', `ap_by_ap', `manual', or 'multitone'
   pc_period          int
   pc_tonemask        n char string, followed by n floats
   ra_offset          float
   ref_freq           float
   samplers           int, followed by up to 8 strings
   sb_win             2 floats
   skip               `true' or `false'
   start              integer
   station_delay      float
   stop               integer  
   switched           `scan_start' or `each_minute'
   t_cohere           float
   use_samples        `true' or `false'
   weak_channel       float
   x_crc              `keep' or `discard'
   x_slip_sync        `keep', `discard', or an integer
   y_crc              `keep' or `discard'
   y_slip_sync        `keep', `discard', or an integer

KEYWORD SEMANTICS

**scan selection**

   skip          if this is set to true in the body of an if_block, then
                 any scans matching the if conditions will be skipped. 
                 Note: as of 99.2.19 fourfit will not properly skip data 
                 if f_group is specified.

**filtering**    determines whether or not each AP is accepted

   max_parity    maximum allowable fraction of bytes in error
   x_slip_sync   maximum # of frames w/ re-sync in reference station
   y_slip_sync      "    "  "    "   "     "     " remote      "
   x_crc         either keep or discard AP if reference time has CRC error
   y_crc           "      "   "    "    "  "  remote      "   "   "    "
   freqs         controls which frequency channels get included in the fit.
                 The letters a-p correspond to the order that the frequencies
                 appear in the root file (assuming 16 channels). With no
                 suffix, DSB is implied, if both sidebands are present.
                 A plus suffix denotes USB, a minus is used for LSB.
                 After 26 channels, the uppercase alphabet is used,
                 then 10 digits, finally '$' and '%' (i.e. 64 channels).
   index         alternate method used to select data channels, based on the
                 original corel index number. Not as well supported as freqs,
                 and is current being phased out.
   start         start time for data to be included.
   stop          stop    "   "    "  "   "    "
                 Arguments of start and stop are integers with an optional
                 minus sign. A positive integer is interpreted as an
                 absolute time in seconds past the hour (of the scan
                 start time). When a minus sign precedes the start time
                 it is considered to be a time relative to, and later
                 than, the scheduled scan start. Similarly, a negative
                 stop time precedes the scheduled scan stop time, by
                 the indicated number of seconds.
   switched      turns on (frequency) switched mode, which discards some AP's
                 and keeps others, depending on a gating waveform
   period        period in seconds of the gating waveform
   gates         for each freq. channel, the starting delay and duration, in
                 seconds, of the gating waveform
   passband      lower and upper bounds (in MHz) of the spectral passband of
                 data to be accepted, specified as RF frequencies. If the
                 lower bound is greater than the upper bound, the range
                 wraps around -- allowing a band in the middle to be
                 excluded.
   dc_block      if set to true, zero out lowest cross-power spectral
                 channel; useful for suppressing DC bias

**search**       control the fringe-searching process

   sb_win        single band delay search window bounds, in us
   mb_win        multiband     "     "      "       "     "  "; if the upper
                 bound (2nd number) is less than the lower bound (1st
                 number), then fourfit performs a "wrap-around" search, in
                 order to handle the case of a delay near to the multiband
                 (semi-) ambiguity.
   dr_win        delay_rate search window bounds, in us/s 
   ion_npts      number of evaluation points in ionospheric coarse search
   ion_win       ionospheric coarse search window in TEC units
   ra_offset     apply right asc.offset (asec) to re-center search windows
   dec_offset      "   declination  "   (asec) "      "        "      "
   interpolator  selects method of fit interpolation. Classically, an
                 iterative search has been done over sbd, mbd, drate, one
                 dimension at a time, for 3 cycles. The simultaneous mode
                 constructs a 5x5x5 cube of data points and does a 3D
                 quintic interpolation.


**corrections**  apply corrections to the data, either before or after fit

   pc_mode   specify phase_cal mode:
              - normal (model linear in time is extracted from the data)
              - manual (specified totally by the user) 
              - ap_by_ap (phase cal is extracted independently for each AP)
                DEPRECATED: use normal or manual with pc_period 1 or more
              - multitone (all tones in band are coherently fit, and phase 
                is extrapolated to the center of the band).
   pc_phases phase_cal phases in deg, for each of the listed freq channels;
             these offset phases are added to the underlying model, as
             specified by pc_mode, above. If 2 polarizations are present,
             the same values are applied to both pols.
   pc_phases_l specified in same manner as pc_phases, but the tone phases
             so specified are applied only to the first pol (L, X, or H)
   pc_phases_r specified in same manner as pc_phases, but the tone phases
             so specified are applied only to the second pol (R, Y, or V)
   pc_freqs  phase cal tone frequencies in KHz, for each of the listed
             freq channels iff not in range -64..64. Inside of this
             range, the value is interpreted as a tone #, with 1 being
             the 1st USB tone, 2 being the 2nd USB tone, etc. Negative
             tone #'s are used for LSB tones.
   pc_period in multitone mode (only), the phase can be estimated
             and applied over each pc_period ap's, thus removing slopes
             or other drifts in pcal (default is 9999)
   pc_tonemask - in multitone mode (only):
             The values for pc_tonemask form a bit-masked map of which 
             tones to *exclude* for this frequency channel. Thus 1 
             excludes the lowest tone, 2 the next lower tone, 4 the 3rd 
             lowest tone, etc. A value of 5, for example, would exclude 
             the lowest and the 3rd lowest tones (perhaps 10 KHz and 2.01
             MHz).  
   pc_delay_l a time value in ns representing the difference between the
   pc_delay_r the travel time from the feed phase center to the pcal
             injection point, minus the the travel time from the pcal
             pulse generator to the injection point. It is specified
             separately for the two polarization senses.
   lsb_offset additive phase in degrees, for the LSB relative to the USB;
             often necessary when correlating VLBA data against Mk 3
   ref_freq  specifies a frequency in MHz at which the phase delay
             is determined (default is total LO of first frequency)
   adhoc_phase specify mode of ad hoc phase corrections. No corrections
             are made if this isn't present, or is set to false.
   adhoc_period  For ad hoc sinewave model; the period in integer seconds.
   adhoc_amp      "   "  "     "       "    amplitude in degrees of phase.
   adhoc_tref    For both ad hoc phase models; the reference time in seconds
             past the most recent hour.
   adhoc_poly For the ad hoc phase polynomial model; From 1-6 coefficients
             describing a power-series model in time. (deg/sec^n)
   use_samples   If true, use the sampler statistics (aka state counts) to
             normalize the raw correlation sums to the equivalent analog
             correlation.
   ionosphere specified per station, in TEC (10^16/m^2) units
   t_cohere  coherence time used in fringe fit (default is infinite)
   delay_offs delay offsets (ns) to be applied to each of the listed freq
             channels. This correction is made prefit, similar to pcal.
   samplers  the number of samplers, followed by the freq channel 
             identifiers of channels that share a common sampler are
             grouped together in strings. In multitone mode only, the
             averaged tone-derived differential delays are applied to 
             all channels sharing a sampler.
   optimize_closure modifies fine fringe search so as to minimize the
             contribution of non-closing delay errors to the closure phase;
             can result in poorer single-baseline fits
   station_delay a priori guess at the delay from the pcal injection point
             down to the digitizers (ns).

** miscellaneous functions
   fmatch_bw_pct associate freqs < this percentage of bw together (25% default)
   pc_amp_hcode  generate an H code iff any pcal amps less than this (0.005 default)
   weak_channel  the ratio of single_channel_amp to coherent_sum_amp 
                 below which a G code is assigned to the scan (0.5 default)

SPECIAL KEYWORD VALUES
   ?         wild card character
   keep      32767
   discard       0
   true          1
   false         0
   


SPECIAL FORMATS
   UT-epochs:  UT-epochs are expressed in the format ddd-hhmmss, where all 10
           characters are necessary, including leading 0's if
           appropriate.  This format will match that of a scan directory,
           if the UT-epoch that is being specified is an actual scan time.


GENERAL GUIDELINES

   1) White space is ignored; i.e., multiple spaces and line feeds all
      collapse to a single space.
   2) Multiple commands per line are fine.
   3) Comments: anything from an asterisk through the end of the line
      is ignored.
   4) Nested ifs are not allowed (or necessary). Nested parentheses in
      an if condition are fine (NYI).
      As of 94.1.16, parentheses are not supported. The logical operators,
      in decreasing order of precedence are (not, and, or).
   5) Wildcard "?" matches any single character for f_group, station, or
      baseline, any string (of up to 8 characters) for source, and any
      time-value for scan.
   6) Phase cal and delay offsets are treated station by station. 
   7) Only freqs that are chosen for both stations in a baseline are 
      present in the fit.
   8) If multiple if-blocks match a particular passes' choice of baseline,
      f_group, source, and scan criteria, then the later values assigned
      to each parameter overwrite the earlier ones.