The Mk4 data file IO library (DFIO library) handles all disk IO for
the Mk4 data files.  This includes file types 0 to 4.  The goal of
the library is to provide an interface between the disk files and
C structures in memory.  The format of the C structures is kept as
stable as possible, with modifications taking the form of additional
fields, not replacement or deletion of fields.  In this way, application
code remains largely unaffected by data format changes, rendering
a data format version control system feasible.

Overview
--------

The Mk4 system will not see production data handling until 1996 at
the earliest.  For this reason, the design assumes the availability
of fast CPUs and large amounts of physical memory in the host 
computers.  Execution times will be increasingly dominated by the
overhead of disk IO, so the library must be efficient in this area.
The model for the library is that all data files will be read in
their entirety, in one go, maximizing the throughput for files 
stored contiguously on disk.  The data are stored in memory, and
C-structures (which we will refer to as overlay structures) are 
overlaid on the data by the library.  The overlay structures will
be an image of the disk format, and different structures will be
defined for different version numbers of the records in the file.
The library is responsible for selecting the correct overlay structure,
and using its contents correctly.  Initially, the overlay structures 
will be the same ones used by application programs (application
structures).  As the software and the data formats evolve, however, 
the overlay structures will diverge from the application structures, and
a translation step will be necessary.  

The architecture could be simplified by keeping separate overlay
structures and application structures from the start, and performing
a translation step from the start.  This, however, is wasteful of
memory, since space for two copies of each file would be required.
Instead, overlay structures and application structures will start
life as one and the same, and will diverge only when evolutionary
requirements dictate.  The hope is that for the most part, they will
not diverge.  Thus in most cases, the filling of an application
structure (the goal of the library) is a simple matter of setting
a structure pointer to the correct address.  All application structure
declarations in mk4_data.h are done in terms of pointers for this
reason.

The philosophy of reading the entire file in one go has the advantage
of simplifying the use of variable-length records, because one would
not have to determine the record length before reading it.  Since 
variable length records will be common in the Mk4 system, this is an 
useful attribute.

Two disadvantages of the approach are apparent.  First, some type-1 
files could grow very large.  This might strain even modern systems, 
and at the very least force the use of inefficient virtual memory.  
Second, some applications may need only a small fraction of the 
information in a file, and it would be very inefficient to read the 
whole file in such a situation.  The library therefore probably needs 
a mechanism for reading only a subset of certain types of files.  Such 
cases could be handled on an individual basis (this is done for type-2 
files in the Mk3 BFIO library, via the routine read_fringe_quick.c).
In the initial implementation, type-1 files will be read in one go.
If and when the processing of large spectral line files begins, a
modification to fourfit may be required to read the file in pieces.

The reading of the file is to be handled by two generic routines,
open_datafile() and read_mk4file().  The first opens the file, reads the
type_000 record which should occupy the first 64 bytes, and does as
thorough a job of checking things out as possible before either
reporting a problem, or returning a valid stream pointer (or file
descriptor, depending on how the disk read is handled).  The second
routine simply dumps the file into a memory-allocated array as fast
and efficiently as possible.  The exact technique to be used for this
purpose is under investigation.  All Mk4 data files, from type 0 to 4,
will be read in by these two routines.  They will be called by routines
such as read_mk4root(), which take the memory image of the file
returned by read_mk4file() and use it to assign pointers in the
appropriate structure (defined in mk4_data.h).  The application
program will then simply call read_mk4root() and receive a complete
root file structure ready for processing.

Version Control Implementation
------------------------------

To implement the version control system, there are three source files
corresponding to each record type.  The first is $INC/type_xxx.h, 
where "xxx" refers to the record type.  This file defines both the
application structure and the (possibly multiple) overlay structures.
The file also contains defines the symbolic constant Txxx_VERSION,
which indicates which, if any, of the overlay structures is identical
to the application structure.  If none are, the constant is set to
a value of -1.

The second file is $DFIO/addr_xxx.c, which takes the address of the
raw memory image of a disk file record, and a record version number.
It checks to see if the application structure matches the raw memory
image, and if so it simply returns the address of that image.  This is
the direct memory overlay technique used in Mk3 software.  If the
structures do not match, the routine uses the appropriate
overlay structure instead, based on the version number, and copies
structure elements into a memory-allocated application structure.
It then returns the address of the memory-allocated application
structure.  The calling program cannot tell the difference between
the two methods, but instead simply receives a filled-in application
structure address.

The third file is $DFIO/write_xxx.c, which takes an application
structure and an open file descriptor.  It copies the data, if
necessary, into a statically declared overlay structure of the
latest version number, and writes the filled structure directly
to disk.  It skips the copying step if the application structure
is the same as the latest overlay structure, and instead writes
the application structure to disk directly.

In order to modify the disk-based format, these three files must
be modified.  The new format must be defined in a new overlay
structure in $INC/type_xxx.h, probably accompanied by additions to
the application structure and adjustment of Txxx_VERSION.  New
code to copy the structure elements to and from the new overlay
structure must be written in the addr_xxx.c and write_xxx.c source
files.  Most of this coding will be largely replication
of existing structure definitions and structure element copying
code, and will thus be quick and easy.  Any new or altered fields in
the application structure must be used appropriately in the application.  

There is an important exception to the use of this mechanism.  Because
of its central function in file identification and verification,
the format of the type_000 record is frozen, and the routine
addr_000.c does not exist.  The files write_000.c and type_000.h
are simple, and do not allow for different versions.

Other considerations
--------------------

In the August 24 meeting, the idea of translating Mk3 files into Mk4
memory structures was discussed.  This has the benefit of allowing
applications like fourfit to be largely independent of the origin
of the data, Mk3 versus Mk4.  The tradeoff is between the effort
required to develop the translation routines and the effort required
to maintain working Mk3 versions of fourfit and other programs.  The
former is a known quantity.  The volume of code required is high, but
most of it is fairly simple, consisting of simple copying of structure
elements.  However, there are some fundamental differences between
Mk3 and Mk4 which may not translate easily if at all.  This is a
significant task whose priority would have to be assessed.  The cost
of maintaining Mk3 versions of programs is largely a policy matter.
It would be a simple, if perhaps unpopular, measure to declare that
maintenance of Mk3 software would be limited to fixing bugs, and
that no new functionality would be developed.  Fourfit is the main
problem ... other programs make relatively trivial use of the 
affected code.  In my view, the decision between maintaining Mk3 code
and developing a Mk3-Mk4 translator is not a pressing one.  Nothing
we contemplate doing in the next several months forecloses our
options.  When in doubt, procrastinate.